## Slide 1
District of Columbia Water and Sewer Authority
George S. Hawkins, General Manager
July 14, 2015
Commission for Environmental Cooperation of North America
Joint Public Advisory Committee
Panel II: Adapting to Changing Stormwater Quantities Through Land-use Planning
Briefing for:
DC Clean Rivers Project Overview
Briefing on:

## Slide 2: Separate and Combined Sewer Systems
100% of suburbs
67% of DC
0% of suburbs
33% of DC
2 Pipe System
1 Pipe System

## Slide 3: Background: Combined Sewer Area
Combined Sewer Drainage Area
CSO Outfall
Blue Plains
Municipal Separate Storm Sewer System (MS4) Area
1/3 area is combined (12,478 acres)
47 CSO outfalls
  13 to Anacostia
  10 to Potomac
  24 to Rock Creek
Three receiving waters
  Anacostia River
  Potomac River
  Rock Creek

## Slide 4: Background: DC Clean Rivers Project (LTCP) Development
1998 - LTCP Started
2002 – Final LTCP
2005 – Consent Decree Signed
Public Participation
2007 - New Nitrogen limits require changing LTCP
2003 – LTCP Meets WQS (EPA/DC)
2011 - DC Water begins evaluating GI for Potomac and Rock Creek
LTCP implementation
Total Nitrogen implementation
May 20, 2015- EPA/DOJ lodge Consent Decree Modification in District Court
2014 - DC Water proposes changing LTCP to include Green Infrastructure
DC Water working with DOJ/EPA throughout development and implementation.

## Slide 5
Complete by 2030
DC Clean Rivers Project: $2.6 Billion
Nitrogen Removal: $950 Million
Total > $ 3.5 Billion
20 yr implementation (2005 – 2025)
96% reduction in CSOs & flood relief in Northeast Boundary
Approx 1 million lbs/yr nitrogen reduction predicted
DC CLEAN RIVERS PROJECT AND
NITROGEN REMOVAL PROGRAMS
DC Clean Rivers Project

## Slide 6: DC Clean Rivers has let more than $1.3 Billion in Construction and Engineering Contracts
Blue Plains Tunnel
Poplar Point PS
Anacostia River Tunnel
Main PS Diversions
Tingey St Div. Sewer
CSO 007
CSO 019
Northeast Boundary Tunnel
M St Div. Sewer
First St Tunnel
JBAB Diversions
J
Legend
Completed
Construction
Design
LID at DC Water Facilities
A Blue Plains Tunnel
B Tingey Street Diversion Sewer
C CSO 019 Overflow and Diversion Structures
D JBAB Overflow and Diversion Structures
E M Street Diversion Sewer (CSOs 015, 016 and 017)
G CSO 007 Diversion Structure and Diversion Sewer
H Anacostia River Tunnel
I Main Pumping Station Diversions
N LID at DC Water Facilities
P First Street Tunnel
J Northeast Boundary Tunnel
S Irving Street Green Infrastructure
Y Blue Plains Dewatering Pumping Station and ECF
Z Poplar Point Pumping Station Replacement

## Slide 7: Project Benefits: CSO Reduction
Chart: CSO Overflow (mg/avg year)
| Anacostia River | Potomac River | Rock Creek | Total System
1996 | 2142 | 1063 | 49 | 3254
2015 | 1282 | 638 | 48 | 1968
LTCP Completed | 54 | 79 | 5 | 138

## Slide 8: Project Benefits: Flood Relief
Rhode Island Metro
First & P St NW
Flagler St NW
Rhode Island & T St NW
Rhode Island Between First & 2nd St
Rhode Island & T St NW
Rhode Island & First St NW
First & V St NW

## Slide 9: Project Evolution
58 mg Potomac Tunnel
(CSO 020-029)
Pump Station
9.5 mg Piney Branch Tunnel
126 mg Anacostia Tunnel System
Pump Station
Manage volume equivalent to 1.2” falling on 365 impervious acres
Separate CSO 025-026
225 mgd Pump Station and Enhanced Clarification Treatment
157 mg Anacostia Tunnel System
Existing Consent Decree
Consent Decree Modification
30 mg Gravity Potomac Tunnel
Manage volume equivalent to 1.2” falling on 133 impervious acres
for CSO 027, 028, 029

## Slide 10: Irving Street Green Infrastructure Project
To help mitigate flooding in the Bloomingdale area, the DC Clean Rivers Irving Street Green Infrastructure Project included:
  Installation of 14 bioretention facilities
  Located along Irving Street corridor between Michigan Avenue and North Capitol Street
  Approx. 400,000 gal of storage provided
Flooding in Bloomingdale and LeDroit Park
Recently planted bioretention

## Slide 11: Previous Experience – Indianapolis
Pogue’s Run
Multipurpose project: provided control for CSOs and flooding
Offline basins store peak storm water flows
Reduction in peak flows allows conversion of downstream culvert to CSO storage facility
Green Infrastructure and Sewer Separation implemented on smaller scale for localized control
I-65
I-70
I-70
I-65
WHITE RIVER
POGUE’S RUN
OFFLINE STORMWATER DETENTION FACILITIES
2.2-MILE CULVERT (1915)
ONE BARREL RETROFITTED FOR CSO CONTROL

## Slide 12: Previous Experience – Indianapolis
Benefits Realized
Reduction of flood hazards, insurance requirements, etc.
Improved water quality
  CSO reduction
  Peak storm flow reduction
  Engineered wetland filtering
Improved recreational and educational opportunities
  Property with history of crime and illegal dumping converted to community amenity

## Slide 13: Added Environmental, Social, and Economic Benefits
Environmental
Reduce runoff
Social
Enhance aesthetics
Economic
Create green jobs
Improve air quality
Reduce summer temperatures
Reduce energy usage
Offset climate change
Habitat improvement
Enhance property values
Improve quality of life
Improve liveability through green space
Reduce scope and duration of disruption during construction

## Slide 14: Approach to Adapting to Climate Change
Technologies selected based on strengths
  Small CSOs, less dense areas – GI
  Large CSOs, ultra dense areas – gray infrastructure
GI addresses water at the source and leaves space for downstream technologies if needed for additional control
Conservatism in design – 20% safety factor
Interconnected tunnel system with live pumping is more resilient to changing weather patterns
Gravity system (rather than reliance on pumping station) more reliable and provides redundancy

## Slide 15: Questions?